MACHINE No. 410w110

NEEDLE BAR TAKE-UP. HIGH SPEED.    LONG ARM.    DROP FEED. SINGLE NEEDLE. SINGLE THREAD CHAIN STITCH. FOR BASTING AND STITCHING MEDIUM AND MEDIUM HEAVY WEIGHT FABRICS.

MACHINE No. 400w108

HIGH SPEED. LONG ARM.

DOUBLE ROTARY DISC TAKE-UP SINGLE NEEDLE. LOCK STITCH. DROP FEED.

MAXIMUM STITCH 5 1/2 TO THE INCH. NEEDLE BAR STROKE 1 9/64 INCCIES. PRESSER BAR LIFT 5/16 INCH FOR STITCHIING MEDIUM AND MEDIUM HEAVY FABRICS

MACHINE No. 400w101

DOUBLE ROTARY DISC TAKE-UP. HIGH SPEED.

SINGLE NEEDLE.  LOCK STITCH.  DROP FEED. LONG ARM.

NEEDLE BAR STROKE I 9/64 INCHES. PRESSER BAR LIFT 9/32INCH.

FOR STlTCHING LIGHT AND MEDIUM WEIGHT FABRICS.

MACHINE No. 400w102

DOUBLE ROTARY DISC TAKE-UP. HIGH SPEED.

SINGLE NEEDLE.  LOCK STITCH.  DROP FEED. LONG ARM.

NEEDLE BAR STROKE 1&13/64 INCHES PRESSER BAR LIFT 5/16 INCH.

FOR STITCHING MEDIUM AND MEDIUM-HEAVY FABRICS.

MACHINE No. 400w103

DOUBLE ROTARY DISC TAKE-UP. HIGH SPEED.

SINGLE NEEDLE.   LOCK STITCH.  DROP FEED LONG ARM.

NEEDLE BAR STROKE 1&7/16 INCHES. PRESSER BAR LIFT 3/8 INCH FOR STITCHING HEAVY AND EXTRA-HEAVY FABRICS.

MACHINE No. 400wl

DOUBLE ROTARY DISC TAKE-UP HIGH SPEED

SINGLE NEEDLE.  LOCK STITCH.  DROP FEED.

FOR STITCHING LIGHT AND MEDIUM WEIGHT FABRICS